Fault Finding my IC251 power supply.

Find diagram here.
Find Icom description at end of instruction manual.
Mt ICOM just stopped working so I removed the link plug at the rear and plugged in a 12v supply and used it for some while.

Now I decided to repair the power supply so removed it from the case of the 251.
It connect to the main body (electrically) by a single 5 way connector.

You can reconnect it while its outside the case.

There are two boards to play with. The first board is a mains filter and DC unit.
Be careful with the two boards as the have mains all over them.

My first problem was now the unit kept blowing fuses. This turned out to be the pillar that should be soldered to the board was not and and was loose. It being chassis and therefore ground was touching the adjacent track which is connected to the yellow wire and is the mains supply in. Once I cleared this problem by soldering the stand-off back to the board no more fuses blew.

One problem fixed now to the main problem.
I tried to measure the -110 and +110v out of this first board but only got some 24v between them. This seems to be the ripple but measuring from ground to each then you get -110v and +110v respectively so I assume this is OK. I haven't looked at the reference output at this point but don’t suspect it.

Now into the metal box. Out with all the screws. The devices in here are the pulse width modulator most suspect (16pin dil) and the two drive transistors on a heat sink but they measure ok in situate. I have ordered a new IC and driver trannies and while I wait I have removed the IC and inserted a 16pin dil socket. The other device on a heat sink IOF 2S07 doesn’t seem to be available but its only a common cathode double diode rectifier.

Replaced the Modulator and tested it. Now I get 12.318 v out great all fixed?
Well as with most things claustrophobia struck. I put it all back in the case and connected the tcvr. Now it blows the mains fuse…...