Kenwood ACC1 wiring in particular the TS790.

Female
9 way	D type	6 Pin Din
Pin 1 n/c	Pin 1 GND
Pin 2	RXD	Pin 2 TXD
Pin 3	TXD	Pin 3 RXD
Pin 4 n/c	Pin 4 ┐
Pin 5 GND	Pin 5 ┘
Pin 6 n/c	Pin 6 n/c
Pin 7 n/c
Pin 8 n/c
Pin 9 n/c

        wiring view

A three wire connection is all that is required at the TS 790 end.
If a USB cable to rs232 9 way D type is used then connect as above. Cable proved with FLDIGI and set Baud rate to 4800 8n1.